## Slide 1: A novel cost function: Correntropy

## Slide 2: Motivation
Mean Squared Error (MSE) is the gold standard of cost functions
Is it good enough? O merely practical?
Is MSE close to the demands of real-life applications? (Non-Gaussianity, Non-linearities)
MSE only takes into account second-order statistics
Alternatives: L1-based cost functions (sparseness), Entropy, and Correntropy

## Slide 3: Correntropy
Generalized similarity measure between random variables X and Y (Cross-Correntropy):
k(.,.) is any continuous positive definite kernel
The expected value is over the joint space
Term coined by CNEL
Elegant formulation of local and global interactions
Takes into account higher-order statistics

## Slide 4: MSE vs Error Correntropy
E = Z – Y (desired minus predicted/estimated)

## Slide 5: MSE vs. Error Correntropy
The error square is weighted by the PDF of the error
However, the quadratic increase for values away from z=y ends up amplifying the contribution of samples far away from the mean
MSE is optimal for Gaussian distributed residuals (or other short-tail PDFs)
Long-tail PDFs, nonsymmetric PDFs or outliers make MSE suboptimal

## Slide 6: MSE vs Error Correntropy
E = Z – Y. Special case: Gaussian Kernel

## Slide 7: Maximum Correntropy Criterion (MCC)
When sampling from densities:
Correntropy emphasizes contributions along z=y (zero error), AND exponentially attenuates contributions away from this line -> controlled by kernel width (sigma for Gaussian kernels)
Goal: Maximize Error Contropy

## Slide 8: Correntropy-based Adaptive Filters

## Slide 9: Maximum Correntropy LMS
Cost function:
Gradient Ascent:
Estimated Gradient:
Instantaneous Update:

## Slide 10: System Identification
Unknown Plant. Compare MSE, MEE (Minimum Error Entropy) and MCC
Impulsive noise:

## Slide 11: Noise Cancellation

## Slide 12: MSE-LMS vs MCC-LMS
Equal computational load
MCC more robust under additive impulsive noise and/or non-stationary environments
MSE-LMS: 1 free parameter,
MCC-LMS: 2 free parameters,
MCC-LMS: Performance surface depends on input AND kernel parameter

## Slide 13: Correntropy Induced Metric (CIM)
Correntropy is not a metric on its own. It is a similarity measure
It is possible to build a metric based on Correntropy:
2 points are close, CIM L2 norm (Euclidean zone)
Outside Euclidean zone, CIM L1 norm (Transition zone)
2 points further apart, CIM L0 norm (Rectification zone)

## Slide 14: CIM

## Slide 15: Kernel Width Influence
It controls the shape of the performance surface
It controls the CIM zones and their limits
It controls the local behavior of Correntropy
Large kernel width  MCC equivalent to MSE
It can be chosen heuristically: Silverman’s Rule, Kernel annealing, Application dependent.
It can be adapted in the system

## Slide 16: Composite adaptation

## Slide 17: Conclusions
Correntropy provides a robust cost function for adaptive systems
It performs better than MSE in non-stationary and/or additive impulsive noise scenarios
MSE can be regarded as a particular case of MCC
Correntropy is local whereas MSE is global
Free parameter can be chosen to investigate properties of systems/signals

## Slide 18: References
All material was adapted and summarized from:
Liu, Weifeng, Puskal P. Pokharel, and José C. Príncipe. "Correntropy: properties and applications in non-Gaussian signal processing." Signal Processing, IEEE Transactions on 55.11 (2007): 5286-5298.
Singh, Abhishek, and Jose C. Principe. "Using correntropy as a cost function in linear adaptive filters." Neural Networks, 2009. IJCNN 2009. International Joint Conference on. IEEE, 2009.
Principe, Jose C. Information theoretic learning: Renyi's entropy and kernel perspectives. Springer Science & Business Media, 2010.